## Slide 1: AAML Final Project - Pruned Wav2Letter

## Slide 2: Outline
Challenge
Methodology
Evaluation Result
Conclusion

## Slide 3: Outline
Challenge
Methodology
Evaluation Result
Conclusion

## Slide 4: Challenge
X10
Pruned Wav2Letter

## Slide 5: Challenge
Baseline (Software) Convolution
  Multi-level for-loops (out_y / out_x / out_ch / filter_y / filter_x / in_ch)
  Each MAC is surrounded by address computation, boundary checks, and loop-control overhead.
acc += filter_val * (input_val + input_offset);
#MAC≈B⋅OH⋅OW⋅OC⋅FH⋅FW⋅C_in/group​

## Slide 6: Outline
Challenge
Methodology
Evaluation Result
Conclusion

## Slide 7
Quantization
operate
C0
CFU
Buffer A0
Buffer A1
Buffer B
C1
TPU 0
TPU 1
TPU 2
TPU 3
C2
C3
Buffer A2
Buffer A3
HW Architure & SW implement
Quad-Core Data Parallelism
  Utilizes a SIMD-like architecture with 4 parallel TPU cores driven by software scheduling.
  Distributes output pixel computation (M-dimension) across cores using QUAD_CORE_STEP to maximize hardware utilization.

## Slide 8: ISA (OP code)
OP_1: Set Input Offset
OP_2 / 7: Set K, N / M
OP_3 / OP_13 / OP_20 / OP_25: Write Buffer A0–A3
  Write packed input to A buffers of each TPU
OP_4: Write Global Buffer B
  Broadcast to all TPU cores
OP_10: TPU Start Computing
  Launch 4 TPU cores simultaneously
OP_5 / OP_15 / OP_22 / OP_27: Read Buffer C0–C3
  Read accumulator results from each TPU
OP_6 / OP_8: Set quantization parameters
OP_9 / OP_11: Quantize and activate output

## Slide 9: Conv
OP_3: Write A0 buffer
A[ 0 : M0−1 ] × K
OP_13: Write A1 buffer
A[ M0 : M0+M1−1 ] × K
OP_20: Write A2 buffer
A[ M0+M1 : M0+M1+M2−1 ] × K
OP_25: Write A3 buffer
A[ M0+M1+M2 : M−1 ] × K
1 | 2
3 | 4
5 | 6
7 | 8
A0
A1
A2
A3
K_size
M_size

## Slide 10: Conv
OP_4:
Write global B buffer
1 | 2
3 | 4
B
K_size
Ｎ_size

## Slide 11: Conv
OP_10:
Launch 4 TPU cores simultaneously
When input and weight buffers are ready, we issue OP_START to launch all four TPU cores simultaneously.

## Slide 12: Conv
OP_5: Read C0 buffer
C[ 0 : M0−1 ] × N
OP_15: Read C1 buffer
C[ M0 : M0+M1−1 ] × N
OP_22: Read C2 buffer
C[ M0+M1 : M0+M1+M2−1 ] × N
OP_27: Read C3 buffer
C[ M0+M1+M2 : M−1 ] × N
7 | 10
15 | 22
23 | 34
31 | 46
C0
C1
C2
C3
N_size
M_size

## Slide 13: Conv
OP_6 / OP_8: Set quantization parameters
OP_9 / OP_11: Quantize and output
acc is the accumulator value read from the C buffer, which is then processed by bias addition, quantization, activation, and finally written back as the output.

## Slide 14: Leaky Relu
Left: Software-only implementation of quantization and activation using MultiplyByQuantizedMultiplier, branch on sign, then clamp in software.
Right: Quantization and activation offloaded to CFU hardware.

## Slide 15: Outline
Challenge
Methodology
Evaluation Result
Conclusion

## Slide 16: Evaluation Results
Original
Latency speedup = 139.64
Ours

## Slide 17: Outline
Challenge
Methodology
Evaluation Result
Conclusion

## Slide 18: Conclusion
The current design is primarily limited by buffer I/O overhead (data loading and unloading).
Future work could focus on implementing burst mode transfers by holding the CMD signal high, allowing for continuous data streaming to the buffer and significantly reducing handshake overhead.
It may be necessary to implement a FIFO to enable continuous data streaming into the buffer.

## Slide 19
Thanks for listening